Luxé Cannon 300Z IP RGBAL
300w Ellipsoidal with Motorized Zoom and Shutters

User Manual

# 1. Introduction and Setup
## Unpacking
After receiving the device, please check whether any visible damage was caused during transport. lf the power cord, housing or the light are damaged, do not operate the device. Contact your dealer or GAMMA LED Vision immediately.
Thank you for choosing our Luxé Cannon 300Z IP RGBAL. This light is designed by high strength die-casting aluminum which is able to endure high temperatures, and is designed in a stylish form.

It uses high power Red, Green, Blue, Amber, and Lime LED’s for, low power consumption, high brightness, and excellent colors. The Luxé Cannon 300Z IP RGBAL features DMX512 control, standalone, and sound-active modes.

For your own safety, please read this manual before installing or using the device. This manual covers the important information on installation and applications. Please install and operate the fixture with following instructions. Meanwhile, please keep this manual for future needs.

### In the Box:
Luxé Cannon 300Z IP RGBAL -	1 pc
PowerCon Power Cable	-	1 pc
DMX Cable 3 Pin	-	1 pc
## Mounting and Operation
Use a clamp rated for the full weight of the Luxé Cannon 300Z IP RGBAL to hang the fixture from the mount(s) on the fixture’s yoke.
As an added safety measure be sure to attached at least one properly rated safety cable to the fixture using on of the safety cable rigging point integrated in the base assembly or on the yoke.
## Safety Precautions
Caution: For added protection mount the fixtures in areas outside walking paths, seating areas, or in areas were the fixture might be reached by unauthorized personnel.
Before mounting the fixture to any surface, make sure that the installation area can hold a minimum point load of 10 items the device’s weight.
Fixture installation must always be secured with a secondary safety attachment, such as an appropriate safety cable.
Never stand directly below the device when mounting, removing, or servicing the fixture.
From a ceiling, or set on a flat level surface (see illustration below). Be sure this fixture is kept at least 0.5m (1.5ft) away from any flammable materials (decoration etc.).
Always use and install the supplied safety cable as a safety measure to prevent accidental damage and/or injury in the event the clamp fails.
∙Don’t try to modify the fixture without any instruction by the manufacturer or the appointed repairing agencies.
∙Warranty is voided if there are any malfunctions from not following the user manual while operating or any hazardous operation, like shock short circuit, electronic shock, lamp broken, etc.

Allow the Luxé Cannon 300Z IP RGBAL LED to cool for at least 15 minutes before handling after use.
## Customer Support
WARRANTY POLICY
GAMMA LED Vision warrants its products for the periods set below from the date of purchase to be free of manufacturer and workmanship defects. Warranty does not cover normal wear and tear caused by force, negligence or misuse of products. GAMMA LED Vision is not responsible for any damages or injury caused by misuse or improper handling of the products and in accordance with instructions and specifications of manual.
Warranty terms are as follows:
LED Fixtures:
Indoor: 2 Years
Outdoor (IP 54 or higher): 1 Year
Lamp Fixtures: 1 year / excludes the lamp
LED Video Products:
Indoor: 2 Years
Outdoor (IP 54 or higher): 1 Year
Controllers: 2 years
Batteries: 6 months
All Trussing Related Products and Accessories: 1 Year
Please visit WWW.GAMMALEDVISON.COM for complete Limited Warranty terms and contact information.
# 2. Setup and Operation
## Using the LCD Menu and Buttons
The menu is accessible via the touchscreen interface. If presented with a lockscreen, the password is +, -, +, -, Enter. (Plus, Minus, Plus, Minus, Enter)
## Menu Operation
Use the Menu Key to enter the menu. The chart below shows the main options and explains the settings. Always press “Enter” to confirm any settings changed.

Main Menu Option	Sub-Menu Option	Value	Function
DMX	DMX Address	001-512	Set the DMX Address
	DMX Profile	05CH, 24CH	Set the channel mode
	Motor Control	Value/Channel	Set the values manually for each channel via the menu.
Master	Mixed Color	Set each channel manually	Manual mode – set each color manually from 0-255
	Auto Mode		Auto mode – select the program and speed as desired.
	Sound Mode		Sound-active mode
	White Point		Set manually by color temperature
	Quick Color		Set manually by gel color
	Motor Control		Manually adjust internal motors.
Status			See a variety of status indicators and measurements.
Settings	White Point Edit		***Use only with password from GAMMA LED Vision**
	Reset Calibration		Adjust the motor calibration for each internal motor.
	Dimmer Frequency		Set the PWM Frequency of the LED Dimmer
	Dimmer Curve		Choose the Dimmer Curve
	Over Temperature		Set the Overtemperature shutdown value – Do not change this setting unless directed by GAMMA LED Vision.
	Backlight		Set the backlight brightness for the menu LCD.
	Backlight Timeout		Set the timeout for the factory LCD
	Load Factory Settings		Factory reset of all settings.

## DMX Setup
### DMX Basics
DMX512 stands for digital multiplex 512. This means that 512 channels are controlled digitally through 1 data cable.
A channel is a set of 255 steps that are assigned to control attributes in each light. This may be a color like red, green or blue, and intensity, strobe, pan/tilt or other attributes.
Multiple sets of 512 “universes” may be used. Only 1 universe will travel on a DMX cable, but through networked DMX (Art-Net or sACN E1.31), many universes can travel over a network.
### DMX Wiring
DMX works by connecting 1 or multiple lights to the output of a DMX lighting console or software with a DMX interface.
DMX lights connect in what is called a “daisy-chain”. Your first DMX cable will plug it’s male DMX connector into the female DMX connector on your lighting console. The remaining female connector will then connect to the DMX input on your first light.
You may then connect your next fixture to the output of your first light, and continue the chain.
32 Fixture Rule – DMX only allows you to connect up to 32 fixtures in a single daisy chain for signal strength. Sometimes, depending on the fixtures and cable length, this number is less (or more).
DMX Cables can be 3-pin or 5-pin. These use the same type of data, and in the 5-pin only pins 1, 2, and 3 are used. The cable should be a 2 conductor, shielded cable of at least 110 ohms resistance. Microphone cable is not DMX cable.
Please refer to the diagram below:
For installations where the DMX cable has to run a long distance or is in an electrically noisy environment, it is recommended to use a DMX terminator. This helps in preventing corruption of the digital control signal by electrical noise and reflections. The DMX terminator is simply an XLR plug with a 120 Ω resistor connected between pins 2 and 3, which is then plugged into the output XLR socket of the last fixture in the chain. Please see illustrations below:

## DMX Modes and Configuration
The Luxé Cannon 300Z IP RGBAL has multiple DMX modes, sometimes called “personalities”, “profiles”, or as we will use here “modes”.
In general, modes with more DMX channels offer a greater level of control or options but take up more of your output channels on your lighting console or software.
Modes with less DMX channels often offer less control, but may be plenty for your needs. Depending on your needs and control solution, you may not need channels for automated programs, strobes, or macros – your console may have great effects! In this case, you can use a lesser channel mode and fit more lights per DMX universe.
View the DMX mode charts below to find the mode that best suits your needs.
DMX Channel Mode Sheet:
On the left side of the sheet you will see the different modes and which channel corresponds to each function listed on the right in the given mode.
Luxe Cannon 300 RGBAL
GAMMA LED Vision – DMX Chart

STD Mode (24 Ch)	Basic Mode (5 CH)	Function	Values	Description
1		Dimmer	0-255	Master Intensity Control
2	1	Red	0-255	Red Control
3	2	Green	0-255	Green Control
4	3	Blue	0-255	Blue Control
5	4	Amber	0-255	Amber Control
6	5	Lime	0-255	Lime Control
7		CTC	0-9	No Function
			10-19	Color Temperature Preset 1
			20-29	Color Temperature Preset 2
			30-39	Color Temperature Preset 3
			40-49	Color Temperature Preset 4
			50-59	Color Temperature Preset 5
			60-69	Color Temperature Preset 6
			70-79	Color Temperature Preset 7
			80-89	Color Temperature Preset 8
			90-99	Color Temperature Preset 9
			100-109	Color Temperature Preset 10
			110-119	Color Temperature Preset 11
			120-129	Color Temperature Preset 12
			130-139	Color Temperature Preset 13
			140-149	Color Temperature Preset 14
			150-159	Color Temperature Preset 15
			160-169	Color Temperature Preset 16
			170-179	Color Temperature Preset 17
			180-189	Color Temperature Preset 18
			190-199	Color Temperature Preset 19
			200-209	Color Temperature Preset 20
			210-219	Color Temperature Preset 21
			220-229	Color Temperature Preset 22
			230-239	Color Temperature Preset 23
			240-249	Color Temperature Preset 24
			250-255	No Function
8		Color Macros	0-9	No Function
			10-19	Color Macro Preset 1
			20-29	Color Macro Preset 2
			30-39	Color Macro Preset 3
			40-49	Color Macro Preset 4
			50-59	Color Macro Preset 5
			60-69	Color Macro Preset 6
			70-79	Color Macro Preset 7
			80-89	Color Macro Preset 8
			90-99	Color Macro Preset 9
			100-109	Color Macro Preset 10
			110-119	Color Macro Preset 11
			120-129	Color Macro Preset 12
			130-139	Color Macro Preset 13
			140-149	Color Macro Preset 14
			150-159	Color Macro Preset 15
			160-169	Color Macro Preset 16
			170-179	Color Macro Preset 17
			180-189	Color Macro Preset 18
			190-199	Color Macro Preset 19
			200-209	Color Macro Preset 20
			210-219	Color Macro Preset 21
			220-229	Color Macro Preset 22
			230-239	Color Macro Preset 23
			240-249	Color Macro Preset 24
			250-255	No Function
9		Strobe	0-10	No Function
			11-255	Strobe, Slow to Fast (1-25 Hz)
10		Auto Programs	0-9	No Function
			10-19	Auto Run Preset 1
			20-29	Auto Run Preset 2
			30-39	Auto Run Preset 3
			40-49	Auto Run Preset 4
			50-59	Auto Run Preset 5
			60-69	Auto Run Preset 6
			70-79	Auto Run Preset 7
			80-89	Auto Run Preset 8
			90-99	Auto Run Preset 9
			100-109	Auto Run Preset 10
			110-119	Auto Run Preset 11
			120-129	Auto Run Preset 12
			130-139	Auto Run Preset 13
			140-149	Auto Run Preset 14
			150-159	Auto Run Preset 15
			160-169	Auto Run Preset 16
			170-179	Auto Run Preset 17
			180-189	Auto Run Preset 18
			190-199	Auto Run Preset 19
			200-209	Auto Run Preset 20
			210-219	Auto Run Preset 21
			220-229	Auto Run Preset 22
			230-239	Auto Run Preset 23
			240-249	Auto Run Preset 24
			250-255	No Function
11		Framing Shutter 1 Position	0-255	Inserts Framing Shutter 1
12		Framing Shutter 1 Angle	0-255	Angle Adjustment of Framing Shutter 1
13		Framing Shutter 2 Position	0-255	Inserts Framing Shutter 2
14		Framing Shutter 2 Angle	0-255	Angle Adjustment of Framing Shutter 2
15		Framing Shutter 3 Position	0-255	Inserts Framing Shutter 3
16		Framing Shutter 33 Angle	0-255	Angle Adjustment of Framing Shutter 3
17		Framing Shutter 4 Position	0-255	Inserts Framing Shutter 4
18		Framing Shutter 4 Angle	0-255	Angle Adjustment of Framing Shutter 4
19		Zoom	0-255	Zoom 30° to 15°
20		Focus	0-255	Focus Control
21		Gobo Control	0-255	Optional Gobo Control Accessory
22		Iris Control	0-255	Optional Iris Control Accessory
23		Framing Macros	0-63	No Function
			64-255	Framing Macros
24		Control	0-249	No Function
			250-255	Reset All Motors

# 3. Maintenance
## Troubleshooting Problems
The following are a few common problems that may occur during operation. Here are some suggestions for easy troubleshooting:
A. The unit does not work:
- Check that the unit is plugged in to a working power connector.
- Press the menu button to confirm that the unit is powered on. If the screen does not light up, the unit has no power.
B. Not Responding to the DMX Controller
- Check DMX cables to verify that they are plugged in and functional.
- Check the DMX address and mode – does it match the address and mode patched in the lighting console or software?
- Plug the light directly into the DMX controller with a cable that you know is good. Unplug all other lights – does it work?
- Try to use another DMX controller.
# 4. Technical Specifications
- Rated voltage: 100V-240VAC, 50/60Hz
- Power Consumption:300w Max
- LEDs: 300w RGBAL
- Lamp rated life: >50000 Hours
- Beam angle: 15-30 degree
- Strobe: Independent electronic strobe, 0-20 hz, the speed can be adjusted
- Control Mode: DMX512 control, Auto Run, Master/Slave, Sound-Active
- IP Rating: IP 65
- Net Weight: 44lbs
- Certification: CE, RoHS
- RDM UID: 1901:82B2DC04

# 5. Photometrics:
4300k (High CRI Mix)
CRI: 85.7 CRI

TM30

Illuminance Report:
	At Full – 15 Degree	At Full 30 Degree	High CRI Mix – 4300k, 85.7 CRI – 15 Degree
5’	2930 fc	1040 fc	2450 fc
10’	927 fc	298 fc	885 fc
15’	451 fc	143 fc	435 fc
20’	252 fc	78 fc	235 fc
30’	104 fc	33 fc	98 fc
35’	85 fc	26 fc	79 fc